## Slide 1
SLIDE 1 · PROBLEM STATEMENT & PROJECT OBJECTIVE
2D & 3D Motion Analysis Using a Single RGB-D Camera
Intel RealSense D455f · compact, real-time, single-camera motion analysis
PROBLEM STATEMENT
Traditional motion-analysis systems often rely on expensive multi-camera motion-capture setups or specialized sensors. There is a need for a compact, real-time and accessible system that can capture human movement and extract meaningful joint-level motion data using a single camera.
PROJECT OBJECTIVE
▸ Develop a 2D + 3D human motion analysis system using a single Intel RealSense D455f
▸ Detect human body joints and quantify movement parameters
▸ Support both live camera input and recorded video
▸ Provide a foundation for real-world 3D motion measurement
CURRENT PROGRESS — 2D PHASE COMPLETED
▸ 33 body landmarks detected using MediaPipe Pose
▸ Joint coordinates represented in RGB image pixels (u, v)
▸ Elbow angles calculated in the image plane
▸ Wrist trajectory and pixel velocity calculated
▸ CSV / video output and post-session analysis report implemented
INTEL REALSENSE D455f
Single RGB-D camera · USB 3
2D · COMPLETED
RGB joints, elbow °, wrist path
3D · NEXT PHASE
Depth → camera metres / m/s
Current status · 2D analysis completed → 3D depth-based analysis is the next phase

## Slide 2
SLIDE 2 · SOLUTION & SYSTEM WORKFLOW
Proposed Solution — End-to-End Motion Analysis Pipeline
2D path is built · dashed 3D path is the next phase, not implemented
A single RGB-D camera captures the subject, MediaPipe extracts 33 body landmarks, and the system converts these landmarks into measurable motion parameters.
BUILT · 2D MOTION ANALYSIS
01 INPUT
Live D455f
Uploaded video
two sources, one pipeline
02 RGB FRAME
Colour frame
capture
image plane only
03 MEDIAPIPE
33 landmarks
2D pixels (u, v)
origin: top-left
04 ANALYSIS
Elbow angle (image °)
Wrist trail + px/s
angles + trajectory
05 OUTPUT
Visualization & report
CSV + overlay video
post-session graphs
3D EXTENSION · NEXT PHASE · NOT IMPLEMENTED
2D pixel (u, v)
+ RealSense depth
Depth
alignment
3D
deprojection
Camera
coordinates (m)
3D motion
/ speed
Current implementation: RGB-based 2D motion analysis · Next phase: RealSense depth integration for true 3D coordinates

## Slide 3
SLIDE 3 · TECHNOLOGY STACK & IMPLEMENTATION
Technology Stack & System Architecture
Modular 2D pipeline · hardware, vision, app, data · ready for depth later
HARDWARE
Intel RealSense D455f RGB-D camera · USB 3.0 · future depth integration
COMPUTER VISION & AI
MediaPipe Pose 33 body landmarks · real-time pose estimation
OpenCV Frame processing · video I/O · overlay generation
APPLICATION DEVELOPMENT
Python Core processing pipeline
Tkinter Live UI · camera / file · session control
Matplotlib Post-session graphs · angle / time · statistics
CONFIGURATION & DATA
YAML Central config — camera, pose, analysis, output
CSV / JSON / MP4 Motion data · run metadata · annotated video
ARCHITECTURE
RealSense / Video
Capture layer
Pose estimation
(MediaPipe)
Motion analysis
2D angles
Wrist motion
Visualization
& reporting
CSV / video / report
Built as a modular pipeline → ready for RealSense depth integration in the 3D phase.
Jay · IIT Guwahati · python app.py · config.yaml · 2D implemented, 3D not claimed

## Slide 4
SLIDE 4 · LITERATURE REVIEW
Literature Review — 2D Pose Estimation to 3D Motion Analysis
Two papers: the 2D method we use now · why a single RGB view is not enough for 3D
PAPER 1
BlazePose: On-device Real-time Body Pose Tracking
Bazarevsky et al., Google Research (2020)
WHAT IT PROVIDES
▸ Real-time single-person pose from RGB image / video
▸ 33 keypoints: shoulders, elbows, wrists, hips, knees, ankles
▸ Detector + tracker pipeline for on-device tracking
▸ Aimed at fitness, gesture recognition and AR
LIMITATION FOR OUR PROJECT
RGB pose is 2D image information. Depth cannot be reliably obtained from a single RGB view — body parts moving toward / away from the camera stay ambiguous.
RELEVANCE
Foundation of our current 2D phase through MediaPipe Pose.
PAPER 2
Accuracy Evaluation of 3D Pose Reconstruction through Stereo Fusion for Physical Exercises with MediaPipe Pose
Dill et al., Sensors (2024)
WHAT IT STUDIES
▸ 3D pose reconstruction for physical-exercise analysis with MediaPipe Pose
▸ Two camera views + MediaPipe 2D landmarks + triangulation
▸ Compares reconstructed 3D pose with motion-capture ground truth
▸ Stereo fusion beats monocular 3D estimation
KEY FINDING / LIMITATION
3D from one RGB view is ill-posed: many 3D poses share the same 2D projection. MediaPipe “world” landmarks guess depth from an internal body model and are noisy.
RELEVANCE
Supports moving from 2D image measures to sensor-based 3D (RealSense depth).
Takeaway · BlazePose / MediaPipe is our 2D base → Dill et al.: true 3D needs more than one RGB view — we will use RealSense depth
Literature is exploratory for this progress talk · we have not claimed a full survey