## Slide 1
PROGRESS UPDATE · SINGLE INTEL REALSENSE D455f
2D and 3D Motion Analysis
Problem statement · Assigned: 2D + 3D | Delivered this phase: 2D only
01 THE ASSIGNMENT
Measure human motion with one RGB-D camera.
▸ Hardware: Intel RealSense D455f
▸ Live USB and uploaded video
▸ Camera coordinates (image pixels)
▸ No hardcoding — config.yaml
02 THIS PHASE
Full problem is 2D + 3D. We completed 2D.
▸ 2D = colour frame → joint pixels (u, v)
▸ Origin: top-left of the RGB image
▸ 3D (depth → metres) is not built yet
▸ Student prototype — not a medical device
03 WHY 2D FIRST
3D is the same pixel plus RealSense depth.
▸ If the 2D dot is wrong, 3D will be wrong
▸ So: RGB → keypoints → angles → one app
▸ Then add aligned depth for metres / m/s
▸ Do not treat MediaPipe “world” as RealSense 3D
Jay · IIT Guwahati · 2D phase complete · Next: depth → camera metres

## Slide 2
SOLUTION · 2D APPLICATION
What we built
One window: live D455f or upload · skeleton, elbow degrees, wrist path · optional save
A user-facing 2D app. Thresholds stay in config.yaml. Camera pixels only — not metres, not a medical device.
01 RGB SOURCE
Live D455f
or .mp4 / .avi / .bag
Colour frames only
02 POSE 2D
MediaPipe Pose
33 joints (u, v)
Origin: top-left
03 ANALYSIS
Elbow angle (image °)
Wrist trail + px/s
Skip low confidence
04 OUTPUT
GUI live numbers
CSV + overlay.mp4
Start / Stop
Live or Upload
Elbow ° in the image · ~180° = straight
Wrist speed in px/s · not m/s
Workflow is 2D camera pixels only. Depth is not used yet.

## Slide 3
IMPLEMENTATION
Tech stack
Python · nothing hardcoded in code · run from the project folder: python app.py
CAMERA
Intel RealSense D455f
pyrealsense2 · live RGB
.bag playback for later 3D
VIDEO
OpenCV
Uploaded .mp4 / .avi
Skeleton overlay on RGB
POSE
MediaPipe Pose
BlazePose · 33 landmarks
2D pixels (u, v) only
CONFIG
YAML · config.yaml
Resolution, FPS, thresholds
Which joints and trail
INTERFACE
Tkinter + Pillow
Live / Upload · Start / Stop
Live elbow ° and wrist px/s
DATA OUT
CSV + MP4
keypoints_2d.csv
angles_2d.csv · overlay.mp4
Not used as 3D: MediaPipe world landmarks (RGB-only guess). Real 3D = RealSense depth at these 2D pixels. Close Viewer before Live.
Jay · IIT Guwahati · python app.py · USB 3 · close RealSense Viewer